## Slide 1: DHI-WASY Software Training Modeling Subsurface Flow and Transport using FEFLOW 7.0

## Slide 2: Free vs. Forced Convection
DHI - WASY Software Training

## Slide 3: Exercise 1: Free vs. Forced Convection
Vertical cross section
Salt Intrusion From the Top

## Slide 4: Background
Pressure- vs. density-induced flow

## Slide 5: Spatial Discretization
Dimensionless Characteristics
Forced convection (Peclet number)
Free convection (Rayleigh number)

## Slide 6: Spatial Discretization – Supermesh Setup
(100,-100)
(0,-100)
(100,0)
(0,0)
(42,0)
(58,0)
(42,-5)
(58,-5)
Height 100 m
Width 100 m

## Slide 7: Spatial Discretization
Mesh Generation
Mesh generation with ~3000 (triangular elements)
Local mesh refinement (via Select in Rectangular Region and Select Nodes along a Border tools)

## Slide 8: Model Setup
Problem Settings:
Projection: Vertical, planar (confined)
Problem Class: Fluid flow and mass transport
State: Steady fluid flow, transient transport
Simulation-Time Control: Automatic time stepping, FE/BE time integration, final time: 120,000 days (~330 years)
Solver Settings: Direct equation solver (PARDISO)

## Slide 9: Model Setup
Material Properties: Flow
Density Ratio α:

## Slide 10: Model Setup
Relation between solute concentration and density:
Density ratio a = 10-3
Material Properties: Flow

## Slide 11: Model Setup
Boundary Conditions: Flow
Impermeable border (default)
Hydraulic-head BC at an arbitrary node, e.g., upper left: h = 0 m

## Slide 12: Model Setup
Boundary Conditions: Mass
Concentration at the
spill site: 100 mg/l
Mass-concentration BC along the spill-site border (via Select Nodes Along a Border tool): C = 100 mg/l

## Slide 13: Problem Settings
Reference Values
Set maximum
concentration Cs to 100 mg/l:

## Slide 14: FEFLOW Result
Free convection

## Slide 15: Base Model – Save…

## Slide 16: Model Extension
Head gradient
Horizontal hydraulic gradient (‘strong’)
Implemented as hydraulic-head BC along the left and right vertical borders (Select Nodes along a Border):
• Left side: h = 0 m • Right side: h = 0.1 m

## Slide 17: FEFLOW Result
Flow is dominated by forced horizontal convection

## Slide 18: FEFLOW Results
Reducing the boundary-condition value on the right vertical border (Select Nodes Along a Border):
• Right side: h = 0.01 m
Horizontal hydraulic gradient (‘weak’)

## Slide 19: FEFLOW Results
Combined effects of free and forced (mixed) convection

## Slide 20: Geothermal application
DHI - WASY Software Training

## Slide 21: Exercise 3: Geothermal Application
Salt Intrusion From the Top
Vertical cross section of the model domain
Heat extraction from a sloped sandstone aquifer

## Slide 22: Spatial discretization
Mesh generation 1
3 supermesh polygons
Transport mapping with 3000 quad elements, option Triangulation

## Slide 23: Spatial Discretization
Local refinement within sloped aquifer
Supermesh Polygons > Select by Map Polygons, Set Snap distance = 0 m
Refine elements twice
Mesh generation 2

## Slide 24: Model Setup
Problem Settings:
Projection: 2D vertical, planar
Problem Class: Flow and heat transport
State: Steady flow and transport
Solver: Direct Equation Solver

## Slide 25: Model Setup
Material Properties: Flow
Hydraulic Conductivity:
  1E-7 m/s globally
  1E-4 m/s within the sloped aquifer (select elements by map polygon)

## Slide 26: Model Setup
Impermeable boundaries (default)
One hydraulic-head B.C. at an arbitrary node, upper left border, h = 0 m
Boundary Conditions: Flow

## Slide 27: Model Setup
Implemented as temperature boundary condition on the top and bottom border (Select nodes Along a Border tool)
        Top: T = 20°C
        Bottom: T = 90°C
Geothermal gradient: 35 K/km
Boundary Conditions: Heat

## Slide 28: Model Setup
Reference Values
Reference Temperature
T0 = 20° C

## Slide 29: FEFLOW Result
Conductive Temperature Distribution
 Save as Base model!

## Slide 30: Model Extension
Problem Settings
State: Transient flow, Transient transport
Simulation-Time Control:
  Automatic time-step control
  First-order accurate (FE/BE integration)
  Final simulation time: 36500 days (100 years)
  Error tolerance: 0.1* [10-3], Maximum Error Norm

## Slide 31: Model Extension
Boundary Conditions
Remove h = 0 m hydraulic-head B.C. that was needed for steady-state computation

## Slide 32: Model Extension
Water density as a
function of temperature
Global: Expansion coefficient β = 0.0004 K-1  Input 4 [10-4] K-1

## Slide 33: Base Model – Save…

## Slide 34: FEFLOW Result
 No convection cells

## Slide 35: Model Extension
Material Properties: Flow
Aquifer of higher hydraulic conductivity:
    Conductivity [max] = 50 [10-4 m/s] (Select by map polygon with Supermesh polygons as selection map)

## Slide 36: FEFLOW Result
Convection cells develop in aquifer

## Slide 37: FEFLOW Result
Convection cells develop in aquifer

## Slide 38: Load Model – Save…

## Slide 39: Model Extension
Boundary Conditions
Pumping rate of 250 m3/h, or 6000 m3/d, over 500 m system width: 12 m2/d (2D)
Distributed vertically over 40 m aquifer height, the outflux due to pumping is 0.3 m/d
An inner Neumann-B.C. acts in two directions
simultaneously, thus the B.C. value is half the flux:
q = 0.15 m/d
Pumping (heat extraction) from aquifer and re-injection (of cooled water) into aquifer

## Slide 40: Model Extension
Boundary Conditions
Set 2nd-kind B.C.s (via Select Individual Mesh Items):
Save the respective node selection for both B.C.s (via the context menu of the Spatial Units panel)

## Slide 41: Model Extension
Boundary Conditions
Implemented as 1st-kind B.C. at injection nodes:
Temperature of re-injected water: 20°C
T = 20°C

## Slide 42: Model Extension
  State:
    Transient flow, transient transport
Simulation-Time Control:
  Final simulation time: 20000 days
Problem Settings

## Slide 43: FEFLOW Result

## Slide 44: Model Extensions
Boundary Conditions:
Delete flux BC and injection temperature BC
Problem Settings
Final time: 1,000,000 days
Set observation point at outlet position

## Slide 45: FEFLOW Result

## Slide 46: Thank you